## Slide 1: FIDO: A Low-Cost, Scalable Autonomous Robot for Environmental DNA Sampling and Preservation
Enoch Nicholson, Scott Jensen, Kevan Yamahara, James Birch, James McClure, David Boone, George Stern, Nadia Allaf, Adam Sepulveda
OCEANS Brest
June 18th, 2025

## Slide 2: MBARI (Monterey Bay Aquarium Research Institute)
We are here
Advancing marine science and engineering to understand our changing ocean.
Notes: Good morning, everyone. My name is Enoch Nicholson from the Monterey Bay Aquarium Research Institute
First, who are we…
MBARI is a non-profit oceanographic research institute founded in 1987 by David Packard. We're located in Moss Landing, California, at the edge of the Monterey Bay submarine canyon - one of the deepest underwater canyons on the west coast.

## Slide 3: MBARI (Monterey Bay Aquarium Research Institute)
Scientist and Engineers collaborating and innovating
Notes: At MBARI, we bring together engineers and scientists to develop technology that explores questions like who lives in the water, and how do these communities interact, move and change?
There are lots of tools for studying this, but, today, I am going to focus on one, environmental DNA.

## Slide 4: Environmental DNA (eDNA)
Labor-intensive, weather-dependent, boring
Difficult access, logistically complicated
Notes: Who here has heard of eDNA?
…
As organisms move through the water, they continuously shed genetic material. This leaves a physical trace that we can collect and analyze to identify what species are present, instead of trying to catch or observe organisms directly.
eDNA analysis starts with sample collection, and traditionally, this has been labor-intensive, weather-dependent, and frankly, quite boring work.
This is made even more complicated by difficult access, and complicate logistics.

## Slide 5: Environmental Sample Processor
Complex, expensive, and require significant expertise to operate
2nd Generation ESP
3rd Generation ESP
Notes: At MBARI, we've been working on this problem for almost three decades with our Environmental Sample Processor, or ESP.
The 2nd generation ESP, shown on the left, is a large, instrument designed for long-term stationary deployments.
The 3rd generation ESP, shown on the right made this sampling mobile by bringing it aboard autonomous underwater vehicles.
The goal with both of these instruments was to take laboratory capabilities into the ocean and send data back to shore instead of samples.
Cool…
but they're complex, expensive, and require significant expertise to deploy and maintain. While they are well suited for certain applications, there are a wide range of use cases where our existing tools are not the correct choice.
New applications benefit from new instrumentation.

## Slide 6
Notes: Our partners at The United States Geologic Survey (USGS) came to us with a problem.
Part of their mission is to understand and monitor the biological health of water resources within the United States.
In this context, that means early detection of invasive species.
To do this effectively they need to sample, ideally, daily at the scale of the entire united states.
The combined space and time scales of their goals far exceed their personnel.
What they do have is infrastructure.
Take the largest continental US watershed , the Missouri. About 1000 square km.
Ignore the trees… the dots on this map represent sites where USGS has field sites.

## Slide 7
Notes: A subset of these look like this…
On the left, steam gauge hut
Power, coms, environmental protection…
On the right, the plan…
Install sampling instrumentation at these shore stations, put a hose out into the river

## Slide 8
High Frequency or Long Term sampling
USGS -- repeated deployments in 2018, 2019, 2021, 2022
NOAA -- Scott Creek, McCloud
Carter’s Bridge (Yellowstone R.)
Corwin Springs (Yellowstone R.)
Scott Creek (Santa Cruz, CA)
McCloud River (Shasta, CA)
Notes: We have done this a lot… using the instrumentation that we had
Mostly in the American West
Worked well to prove the concept, but this was not going to scale…
Different requirements… real time detection at sea…

## Slide 9
Courtesy of Adam Sepulveda - USGS
Notes: USGS was well aware of this, and started the READI-Net program to fund the development and implementation of technology to meet their needs

## Slide 10: FIDO: Filtering Instrument for DNA Observation
Hardware:
Affordable
High Capacity
Autonomous
June 2023 - Concept
August 2023 - Alpha
October 2023 - Beta
April 2023 - Kickoff
Software:
Flexible
Simple
Automatic
Notes: The program kicked off at MBARI where we formalized requirements for our new sampler FIDO.
After this meeting we started prototyping…
Over the course of the first year, we developed functional alpha and a beta prototypes and had lots of chances to test them…

## Slide 11: Testing & Validation: Field Tests
Beta FIDO Installed at the Monterey Bay Aquarium
Alpha FIDO Installed on the MBARI Dock
Notes: The alpha FIDO spent a week on our dock drinking harbor water, primarily as a mechanical test.
The beta FIDO spent two days at the Monterey Bay Aquarium sampling one of the exhibits with as part of multi-sampler validation study facilitated by MBARI. That publication should be out soon.

## Slide 12: Testing & Validation: Laboratory Work
dPCR Anchovy and Rainbow Trout
Anchovy
E. mordax
Rainbow Trout
O. mykiss
Notes: Quick science note…
Before we deployed at the aquarium, we validated against standard laboratory vacuum filtration using both digital and quantitative PCR. I’m just showing dPCR here.
We did this for both ocean and fresh water species (anchovy and rainbow trout).
The means matched well enough to continue.
Weird the shape you see is due to a low sample number

## Slide 13: Testing & Validation: Field Tests
Integration on-board RSV Nuyina
Notes: Most recent and most stressful test was a ten week Southern Ocean expedition aboard the Australian Ice Breaker RSV Nuyina where it collected samples twice daily from the ship's underway seawater system.
All of this field work taught us a lot…
The dock and aquarium trials helped us resolve major issues with our fluidic system and helped us figure out how to FIDO simpler and easier to build.
The Antarctic deployment was particularly valuable because it showed us exactly what falls apart when you mail the instrument to the other side of the world.

## Slide 14: Instrument Overview
FIDO Instrument
Sample Puck with RFID Tag
144 Sample Cylinder
Notes: At the start of this year, we completed our production design.
The instrument at its core is quite simple - it's designed to filter water and apply a preservative to the collected sample.
FIDO expands on the puck concept of the second generation ESP.
Samples are collected using small cylindrical pucks that contain standard 47mm filter paper and an RFID tag to store sample metadata.
144 of these pucks are held within a 3D printed interchangeable cylinder.
This cylinder is loaded into the FIDO instrument which is constructed using sheet metal panels and 3D printed components.
By keeping the mechanism cost low, we were able focus our spending on the components directly responsible for collection and preservation, the valves, pumps and pucks.

## Slide 15: FIDO: Instrument Overview
Waste
Container
Used Puck
Storage
Reagent Storage
Sample Cylinder
2G ESP Not FIDO
Washing Machine Not FIDO
Notes: FIDO fits within a ½ cubic meter and was designed to be accessed by users from the front and to fit into tight spaces like the gauge houses I showed earlier.
2G installed inside a big one…
From the front, users can install pucks, access reagents, removed collected samples, and dispose of waste.

## Slide 16: FIDO: Instrument Overview
Sample Outlet &
Flow sensor
Puck
Manipulation
Micropython
Motherboard
Vacuum System
Rock Pi
Notes: If you need to work on FIDO…
The back of the instrument allows access to its electronics and plumbing.

## Slide 17
Prepare
Install
Operate
Service
Recover
Notes: Now that you have an idea of what FIDO is, I think the best way to complete the picture is to walk through how it will actually be used using the USGS use case as an example.

## Slide 18: FIDO: Pucks
Prepare
Notes: Everything starts in the lab.
Pucks are cleaned, assembled, and installed into a cylinder.
Reagent are made and bottled.
This is also where the pucks have their first bit of meta data written to them (serial number, filter porosity, etc)
I mention this because
Important, can be time consuming, can require lots of training (3G)
---
Emphasis on the puck system

## Slide 19
Install
Notes: Once you have everything ready, you need to carry (quite literally) everything out into the field and hook it up.
This could be its own presentation, and is very application specific, so I’m not going to dive into much. I’d be very happy to talk more about this later with anyone who is interested.

## Slide 20
Operate
Notes: Once the instrument is installed, you drop in the cylinder and reagents, close the lid and walk away.

## Slide 21: FIDO: System Architecture
Micropython
Rock Pi
Notes: Users interact with FIDO through a web interface on any device that they have.
Each instrument can be accessed locally or through the cloud. This interface to communicates with a Rock Pi that handles interfacing with the instrument controller running Micropython.
This system lets users plan and schedule sampling as well as collect manual samples.

## Slide 22: FIDO: Instrument Overview
Operate
Grab
Pinch
Filter
Preserve
Notes: When the instrument collects a sample, the following sequence occurs.
The instrument indexes the cylinder to the first tube.
It turns on the vacuum system, and grabs a puck.
Moves it into the clamp and pinches it between two manifolds.

## Slide 23: FIDO: Fluid System & Reagents
Filter
Preserve
Notes: It then collects a sample, letting water flow through the instrument and back to the source.
Sampling ends biased on flow rate, time, or volume.
Once enough water has been sampled, we apply a preservative

## Slide 24
Store
Decontaminate
Operate
Release
Sweep
Decontaminate
Notes: Next we release the used puck and sweep it into storage.
The clamp then closes on itself and decontaminates the flow path using bleach and waits for the next sample.

## Slide 25
Service
Notes: When you’ve collected enough samples, you visit the instrument and retrieve them and reload the instrument with more pucks and reagents.
Back at the lab you start processing.
I highlight this because…
Like preparation… emphasis on the puck system

## Slide 26
Recover
Notes: When your totally done, you get to haul all that stuff out of there.

## Slide 27: Next Steps
Validation is continuing
10 production units are currently being built
Open to collaborate on field deployments
Looking to license to commercial vendor
Notes: Hopefully that gives you a good sense of FIDO and how it works.
Looking forward…
We're continuing validation work
We're currently building 10 production units that will be deployed throughout the United States this year and next as part of the READI-Net pilot program.
Beyond that, we're actively seeking collaborations for field deployments to expand our understanding of FIDO's capabilities across different environments.
Ultimately, we're looking to license this technology to a commercial partner who can make it widely available to the research community. If you're interested in collaborating or learning more, please find me after the presentation.

## Slide 28: Acknowledgments
Notes: This work wouldn't be possible without our fantastic team at MBARI and our partners at USGS. Special thanks to Adam Sepulveda for leading the READI-Net initiative. Funding came from the United States Geological Survey.

## Slide 29: Questions?
Waste
Container
Used Puck
Storage
Reagent Storage
144 Sample Cylinder
Sample Outlet &
Flow sensor
Puck
Manipulation
Micropython
Motherboard
Vacuum System
Roc Pi
Notes: Thank you for your attention, and I'm happy to take questions.