## Slide 1: CARTRIDGE MOLDING ISSUES OF INSERT
6109_NAUTILUS
SEP 6, 2024

## Slide 2: SKETCH OF INVESTIGATION FROM TDTEC- CHAMFER ON INSERT IS TOO BIG
Insert
Thread Top
Chamfer
Core pin
Too big

## Slide 3: SKETCH OF SECTION VIEW OF INSERT
Screw jam

## Slide 4: ROOT CAUSE OF THE JAM- PLASTIC RESIN GO ATTCH ON THE THREAD OF INSERT
Plastic resin attach on the thread of insert through gaps during molding.
Gaps
Gaps
2.70
3.30~3.40

## Slide 5: IS THE 2.70MM HOLE CRITICAL? IS IT OK TO ENLARGE IT UP TO 3.5MM?

## Slide 6: OPTION 1- ENLARGE THE CORE PIN DIEMETER FROM 2.70 TO 3.5MM
3.30~3.40
3.50
Enlarge the diameter from 2.70mm to 3.50mm x 10 plc.

## Slide 7: OPTION 2- No change of 2.70 hole. Reduce chamfer size be covered by the 2.70 core pin.
Gaps
Gaps
2.70
3.30~3.40
2.095
2.60 Max.
Reduce Chamfer to around 0.20~0.30mm.

## Slide 8: OPTION 3- ENLARGE THE 2.70 HOLE & REDUCE THE SIZE OF CHAMFER
3.0~3.5
Keep it for 0.2mm mini.