## Slide 1: MARS2 IPB Current Sense / Control
Brenton Salmi, Sep 2022

## Slide 2: What does it need to do?
4A Maximum load
12 bit ADC measurement (Vref? Assumed 4.096V)
Goal 10’s ms acceptable rise time detection
  eFuse protection of wire/load simulating a thermal fuse

## Slide 3: ADC Information
We have 16 bits but this is way way way more accurate than we should be needing
Each channel capable of 100KSPS?

## Slide 4: IGB PCB = TMCS1101A4BQDR
400mV/A
  4A = 1.6A
+/- 1.5% Maximum Error (Full-Scale+Drift)
Sampled Integrator Output
  The VOUT of the sensor is actually a discrete analog sampled integrator!
  This requires a reconstruction filter on the output to smooth
    Figure 51 shows a 100KHz LPF output in RED
Voltage Reference
  Vs*0.5 is the zero reference

## Slide 5: Voutput – Sampled Integrator

## Slide 6: Current Sensor Output Error

## Slide 7: Required Bandwidth
Goal = Set Aliasing signals below 1 LSB
  10ms rise time observation ability assumed (arbitrary per IP6.2)
    BW = 0.35/Tr = 35Hz effective bandwidth needed
  Minimum Nyquist = 70Hz
  ADC LSB = (0-5V Range Setting) 5V/4096 = 1.22mV
  Per Kevin = We are sampling at 300SPS
    Nyquist Freq = 150Hz
  <1.22mV (LSB) aliased noise requires -64dB attenuation
    Assumes 2Vp-p noise (0 to 5A)
Place a 4th order Sallen-Key at 50Hz and call it good enough
  -30dB aliased signals which would be only ~60mV (150mA) error
    0-5A noise at the aliasing frequency (crazy noise)
  Placing at 50Hz allows some passband rolloff margin from 35 Hz signal
    35hz signal (10ms rise time) -0.5dB attenuation
    At the expense of allowing aliased noise to be sampled (at -30dB)

## Slide 8: Current Sensor LPF Path
-20dB/Dec
-40dB/Dec
-60dB/Dec
-80dB/Dec
SIGNAL
NYQUIST
F(sample)
35Hz (10ms)
150Hz
300SPS
ADC is used for telemetry only
  Non-critical – information only
  Ideal for situational awareness
Sampling Slower?
  To avoid aliasing in 1SPS data I recommend sampling at 300SPS and just averaging the data to 1SPS prior to sending upstream
Sensor BW
80KHz
Signals in red shade will be observed in sampled data (~50LSB) worst case 5Ap-p noise @150Hz

## Slide 9: Ideal 4-th Order Butterworth
-0.5dB @ 35Hz
This is a rough ideal design – Update with real components

## Slide 10: Anti Alias as built 9/27/22

## Slide 11: Vlimit Control (Analog)
Vref
  2.5V = 0A
  4.1V = 4A

## Slide 12: Fault Debouncing Vs. Persistence
Fault Persistence
Meaning
  Trigger fault after x duration of fault occurrence
Inrush susceptible?
  No
Implementation
  Software = Easy
  Hardware = Hard
    Clock counter…
    Analog slew rate charge timer…
Simple Debounce
Meaning
  Trigger fault and latch for x duration
Inrush susceptible?
  Yes
Implementation
  Schmitt Trigger + LPF (input)

## Slide 13: Fault Debouncing Vs. Persistence
Fault Persistence
Simple Debounce
FAULT PERSISTANCE DELAY

## Slide 14: How does RSN do it
Simple RC filter to charge/discharge a capacitor
  Using time constant of the filter
  Adjustable voltage control of time duration
    Could be just a fixed duration for us

## Slide 15: Trigger Timing Methods
RC Charge (RSN Method)
Extremely Simple
Non-Linear
Vcompare susceptible to op-amp input bias current
  4uA produces nearly a volt of error with RC magnitude needed
  Very low Ib op-amps needed
  Temperature effects
Controlled Slew Rate Charge
2 Op-amps + some R/C’s
Linear
Chart: RC Charge Capacitor Voltage Vs. Time
| 0 | 1 | 5 | 10 | 20 | 30 | 40 | 50 | 60 | 70 | 80 | 90 | 100 | 110 | 120 | 130 | 140 | 150 | 160 | 170 | 180 | 190 | 200 | 210 | 220 | 230 | 240 | 250
Vc | 0 | 0.032134 | 0.15862 | 0.3122 | 0.60491 | 0.87934 | 1.1366 | 1.3779 | 1.604 | 1.8161 | 2.0149 | 2.2013 | 2.376 | 2.5399 | 2.6935 | 2.8375 | 2.9725 | 3.0991 | 3.2178 | 3.3291 | 3.4334 | 3.5312 | 3.6229 | 3.7089 | 3.7895 | 3.8651 | 3.936 | 4.0024
Chart: Slew Rate Controled Trigger Voltage Vs. Time
| 0 | 5 | 10 | 20 | 30 | 40 | 50 | 60 | 70 | 80 | 90 | 100 | 110 | 120 | 130 | 140 | 150 | 160 | 170 | 180 | 190 | 200 | 210 | 220 | 230 | 240 | 250
5 V/s | 0 | 0.025 | 0.05 | 0.1 | 0.15 | 0.2 | 0.25 | 0.3 | 0.35 | 0.4 | 0.45 | 0.5 | 0.55 | 0.6 | 0.65 | 0.7 | 0.75 | 0.8 | 0.85 | 0.9 | 0.95 | 1 | 1.05 | 1.1 | 1.15 | 1.2 | 1.25
10 V/s | 0 | 0.05 | 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9 | 1 | 1.1 | 1.2 | 1.3 | 1.4 | 1.5 | 1.6 | 1.7 | 1.8 | 1.9 | 2 | 2.1 | 2.2 | 2.3 | 2.4 | 2.5
15 V/s | 0 | 0.075 | 0.15 | 0.3 | 0.45 | 0.6 | 0.75 | 0.9 | 1.05 | 1.2 | 1.35 | 1.5 | 1.65 | 1.8 | 1.95 | 2.1 | 2.25 | 2.4 | 2.55 | 2.7 | 2.85 | 3 | 3.15 | 3.3 | 3.45 | 3.6 | 3.75
20 V/s | 0 | 0.1 | 0.2 | 0.4 | 0.6 | 0.8 | 1 | 1.2 | 1.4 | 1.6 | 1.8 | 2 | 2.2 | 2.4 | 2.6 | 2.8 | 3 | 3.2 | 3.4 | 3.6 | 3.8 | 4 | 4.2 | 4.4 | 4.6 | 4.8 | 5

## Slide 16: Simulation
RC Charge (RSN Method)
Controlled Slew Rate Charge
Expected =100ms
Got = 100ms
Expected = 80ms
Got = 62ms

## Slide 17: Both methods act as an “Accumulator”
RC Charge (RSN Method)
Controlled Slew Rate Charge

## Slide 18: Method Challenges
RC Charge (RSN Method)
Controlled Slew Rate Charge
Making sure RC time constant is sufficiently accurate over temp/tolerance
Timing “chart” from bench data
  Inaccuracies (tol, input bias, etc…)
  20% capacitor driving – use precision?
Performing stability analysis per the datasheet to ensure rock solid
  Should be just “follow app-note”
Single supply operation shown in app-note
  Just need to redo

## Slide 21: Vlimit Control Signal Debouncer
Desire to remove false trips
  Fast Inrush current
  Noise on a slowly rising signal
Circuit Type | Pro | Con
Schmidt Trigger | Simple | No inrush current protection triggering
RESET Supervisor Schmitt trigger + output timer delay |  | Same as Schmidt trigger since once trigger the timer is causing the output to hold for duration

## Slide 22: RESET Delay Timers
Contains internal hysteresis
Triggers for a MIN time set by CT pin
  Does not “accumulate” fault time
  Will not stop fast transients from triggering

## Slide 23: Backup

## Slide 24: Current Sensor LPF Path
-100dB/Dec
SIGNAL
NYQUIST
F(sample)
35Hz (10ms)
150Hz
300SPS
ADC is used for telemetry only
  Non-critical – information only
  Ideal for situational awareness
Sampling Slower?
  To avoid aliasing in 1SPS data I recommend sampling at 300SPS and just averaging the data to 1SPS prior to sending upstream
  Move f(-3dB) appropriately and sample even slower.
Sensor BW
80KHz
Signals in red shade will be observed in sampled data (~50LSB) worst case 5Ap-p noise @150Hz