## Slide 1: THE MARS Cabled Observatory Engineering Development & Science Missions
Deep Ocean Cabled Observatories
ASPERA Workshop on Underwater Synergies with Astroparticle Physics
24-25 May 2012
Gene Massion
Monterey Bay Aquarium Research Institute
Moss Landing, CA USA

## Slide 2
The Monterey Accelerated Research System
Originally conceived as a test bed for instrument development
Opportunity to gain early experience in observatory operations
8X Science ports, 100 Mbit/sec, 6.5 kW of power total for all ports
Precision time distribution
Deep water - 890 meters
Accessible - 2 hrs from MBARI
Extended geographic coverage with extension cables
Support for a comprehensive workflow process – proposal through development, test, deployment, and operations
In operation since November 2008
Notes: Introduction slide?

## Slide 4: The Motivation for MARS
The US National Science Foundation was funding development of a new generation of high power and high bandwidth observing systems
Entraining and training a somewhat reluctant community to use these new systems was seen by the proponents as one, maybe the, critical step
Gaining early experience in all aspects of observatory development and operation would yield a decent return on investment for future observatories
Helping the science community be successful at MARS and other observatories is the ultimate goal

## Slide 5: MARS Development Process Overarching design goal: Entrain new and traditional users and make them successful at power on
We employed a Systematic Engineering Process without ever using the term “System Engineering”
Step 1: Understanding what our users want and what they need
  Developed a spectrum of user scenarios: simple to “blue sky”
  Developed semi-formal user and design requirements
  Continually evaluated the design against the requirements and the user scenarios
The Cable Plowing/Laying toolsled: An example of what our users want, geographic diversity, driving what we need to provide

## Slide 6: MARS User Workflow Overarching design goal: Entrain new and traditional users and make them successful at power on
Step 2: Understanding how our users work
  Proposal Preparation
    The critical step: No funding, no project
  Design, test, re-design, re-test in their lab
  Stage for pre-deployment testing in the MBARI test tank
  Test, modify as necessary at MBARI
  Stage for deployment, Deploy & Commission
  Operate and Maintain
    recover, redesign, re-deploy as necessary
  Data Management & Distribution
    Explicity not part of MARS scope

## Slide 7: MARS↔Design/Test Cycle
Your deployment team talks to our MARS staff to work out deployment details
  Extension cables need a lot of interaction w/ocean engineers, ROV pilots and ship’s crew
Your network gurus talk to our network
We help make sure you order the right MARS interface cable
We support testing your system in the MBARI test tank using the MARS wet node simulator

## Slide 8: Proof of Concept: SENSORS CTD
SENSORS was a concurrent project aimed at developing “middle-ware”, the software that sits between an instrument in the water and the cyber-infrastructure on shore to enable “plug and work” functionality
We worked with the sensors group to deploy a familiar oceanographic instrument at the same time as the MARS node.
The goal was to show ‘instrument to internet” functionality immediately after power up.
Part of the MARS commissioning process (after deployment) was to power up the sensors CTD
5 minutes after the SENSORS CTD was powered up an all-hands e-mail was sent out with the URL for real time CTD data and plots

## Slide 9: MARS SCIENCE MISSIONS

## Slide 10: Free Ocean Carbon Enrichment Experiment A controlled seafloor CO2 enrichment experiment
CO2 has no atmospheric chemistry, enrichment experiments are relatively easy to carry out on shore
In sea water, the slow reaction kinetics of CO2 perturbations require a long reaction path and solving the CO2 kinetic equations in real time

## Slide 11: Benthic Rover
Respirometer
Chambers
Current Meter
Video Cameras
Tracks

## Slide 12: Benthic Rover
ROVER Science Questions
  Food: What is the quality and quantity of particulate carbon reaching the seafloor?
  Population Response: What responses are elicited in the sediment community by arrival of particulate carbon on the sea floor?
  How do these ecosystem parameters change over time?
ROVER Measurements
  Sediment Community Oxygen Consumption
  Chlorophyll fluorescence of surface sediment

## Slide 13: Rover Results
November 4, 2009
October 31, 2009
28 One day incubations

## Slide 15: Environmental Sample Processor At the molecular level: who is there, what are they doing and why

## Slide 16: DEIMOS: Deep Echo-Integrating Marine Observatory System Understand the daily vertical migrations of zooplankton, predator-prey interactions (e.g. whale-krill), biological flux
Echogram for 2–4 March 2009, with the corresponding metrics plotted below. From top to bottom, metrics are mean volume-backscattering strength (Sv), area-backscattering strength (Sa), centre of mass (CM), inertia (I), proportion occupied (Pocc), equivalent area (EA), index of aggregation (IA) and the number of layers (Nlayers).
Courtesy: John Horne, University of Washington
http://www.acoustics.washington.edu/DEIMOS/

## Slide 17: EITS: Eye-in-the-Sea on MARS Record response to food falls and bioluminescence, observe new species using a highly intensified camera along with natural bait and bait simulators
Courtesy: Ocean Research and Conservation Association
http://www.teamorca.org/cfiles/home.cfm

## Slide 19: MOBB: Monterey Ocean Bottom Broadband Seismometer Extend the range of the Northern California Seismic Network to the western side of the San Gregorio Fault Zone
http://seismo.berkeley.edu/bdsn/mobb.overview.html
Direct Path
Other way around the world
MOBB

## Slide 20: Bottom Pressure Recorder/Tilt Meter Real time monitoring of submarine seismic activity
Courtesy: Oregon State University
NOAA Pacific Marine Environmental Laboratory
http://www.pmel.noaa.gov/vents/geology/mars/

## Slide 21: Other MARS Science Missions
Acoustic modem test bed
Lab for Ocean Observing Knowledge Integration Grid Seismometer
PHOBOS – long term video, current profiles and CTD data
Chinese prototype deep sea observatory
Sediment Event Sensor
Benthic Microbial Fuel Cell
Enhanced pH and Redox Measurement system
SENSORS CTD – middleware research

## Slide 22: The Other End of the Ocean Observatory Spectrum
The Argo system is one of the few (maybe the only) global, 4D Ocean Observing System
Argo provides a quantitative description of the changing state and patterns of the upper ocean heat content and freshwater storage and transport
3500+ floats, $25K USD per float, maintenance = $0 USD float lifetime: ~4 years, system lifetime: decades
The system is being expanded to include biogeochemical measurements e.g., O2, nitrate, pH and bio-optical sensors

## Slide 23: Thanks for listening
MARS is funded by the David and Lucille Packard Foundation and the US National Science Foundation
http://www.mbari.org/mars/
magene@mbari.org