## Slide 1: IMU Daughter Board Design for BEDS

## Slide 2: Steps to Spinning Daughter Board
IMU board design notes
  Level shifters for SPI (3.3V for PIC, 1.8V for IMU)
  VDD: 3.3V or 1.8V (doesn’t matter)
  No reset so FW control of VDD would be nice
  VDDIO requires 1.8V, does not act as reset
  Two interrupt lines
    INT2 to INT_IMU to RD1
    INT1 to IMU_IO1 to RA15
  See also Invensense SmartMotion Hardware User Guide p14
OK
OK
OK
OK
OK

## Slide 3: Parts
ICM-20948
MAX337EEUD level shifters

## Slide 4: Current setup

## Slide 5: Why Was IMU More Difficult than Expected?
FrankenSystem needed for DevKit use with BEDS board for different voltages.
IMU is capable but requires special FW from Invensense, unclear documentation.
IMU Dev Kit
Invensense
IMU ICD-2049
3.3V ->
1.8V
<-
SPI
MCU: modified code
SPI
Mirror
Don’t use
BEDS board
CS
CS
PIC32
CS
Pressure sensor
5V
EN

## Slide 6: Why Was IMU Hard?
FrankenSystem needed for DevKit use with BEDS board for different voltages.
IMU is capable but requires special FW from Invensense, unclear documentation.

## Slide 7
+5V from lab power supply
Red wires: Logical Elegance prototype configuration
6-channes of level shifting
3.3V signals
1.8V signals
8 wires connected to CN1
TDK/ Invensense
DK-20948 Development Kit
MBARI 10020895-MOB3 Mother Board Assembly
Controls VDD (1.8) on ICM-20948 and MAX3378EEUD Level Shifters Tri-State input signal
Proposed addition
One
reserved signal

## Slide 8
ICM-20948:
  Built-in temperature sensor