## Slide 1: 901303 Cytometer technology for autonomous platforms
Tom O’Reilly
Denis Klimov
Francisco Chavez

## Slide 2: Project goals and activities
Look at available and emerging cytometers, microscopes potentially compatible with AUV, ASV
Collaborate with instrument developers and users
Evaluate instruments in lab, at sea
Develop bench-top test bed
Formulate implementation path
  Science use cases
  Buy-vs-build

## Slide 3: Project team
Denis Klimov: Electrical/optical engineering
Francisco Chavez: Science applications
Tom O’Reilly: Project manager, software
Worden, Scholin, Chavez labs

## Slide 4: 2014
Borrowed, evaluated, compared multiple instruments onboard Rachel Carson, in the lab
Bench-top cell phone, fluorescent microscope test-beds
Presented results at project update, 11/2014
Cytometer/microscope evaluations aboard the Carson

## Slide 5: 2015
Collaborating with Jupiter Research Foundation, Wave Glider microscope
Publication with Dr Peter Lopez (NYU)
Refine test-bed microscopes
Complete analysis of 2014 instrument comparisons
Evaluate CellScope (UCB, SCCWRP)
Evaluate improved 4Deep Submersible Microscope
CellScope: pseudo nitzschia
(photo: A. Gellene, USC)
Notes: Instrument comparisons - Improved Seaflow calibration, new Submersible Microscope hardware/software

## Slide 6: MTS Journal article (TechSurge issue)
Invited by Peter Lopez (Flow Cytometry and Cell Sorting Center, NYU School of Medicine)
  Lopez, O’Reilly, Klimov (2015), “Cytometers set sail with sea-going mobile robots”, Marine Technology Society Journal, volume 49, no 3
Unplanned, opportunistic activity
  Some 2015 deliverables likely not delivered this year
Notes: Lopez participated in MTS Ocean Sensors TechSurge workshop 2014 with Bellingham. Lopez was invited MBARI seminar speaker in 2014.

## Slide 7: JRF WG microscope
Coordinated meetings, discussions with JRF
Technical advice to JRF
  Fluorescence imaging, optics
  Sample preparation, etc.
Science application advice
  Discussions with scientists Scholin, Chavez, Vrijenhoek labs
  Sampling at depth, statistics, image analysis, etc.
Discussed plans for 2016 collaboration

## Slide 8: Application scales
1 um
10 um
100 um
1000 um
particle size
0.1 um
Worden
Scholin, Ryan
Vrijenhoek, Haddock
Chavez
Mobile IFCB - funded
PipeCyte - funded
WG microscope
PSI-FI
Submersible microscope
Emerging AUV/ASV cytometer/microscopes
Notes: PipeCyte has 3-year NSF funding
PSI-FI apparently being commercialized in China

## Slide 9: MBARI 2016 mobile cytometer/microscope workshop
Instrument and vehicle experts discuss latest developments
  Instrument designs
  Science applications
  Adaptive sampling with AUV
  Instrument demos?
Sosik and Swalwell are enthusiastic about this
~2-3 days, 10 guests

## Slide 10: Proposed 2016 plan
Host mobile cytometer workshop at MBARI
Survey cell image identification software (e.g. IFCB)
Refine functional prototype
  Cell phone fluorescent microscope (low cost, size, power)
  Sample flow design, lighting, software
Monitor developments, possible collaborations
Some activity might be subsumed by JRF collaboration project
Bench-top fluorescent microscope prototype
Notes: Functional prototype – not ready for deployment (no pressure vessel, vehicle interfaces).
E.g. some of Klimov’s time could be spent studying feasibility of submersible WG microscope

## Slide 11: Questions?

## Slide 12: Synergy with JRF collaboration project
Might develop test-bed with JRF
MBARI has strong interest in subsurface sampling – instrument integration with AUV

## Slide 13: Cell phone microscope (4x objective)
Fine scale in 100 mm increments

## Slide 14: Testbed
X-Y-Z stage
Base plate
Imaging Source cameras:
BW and Color 1600x1200
Blue LED
White LED
Microscope objective
Lens tube

## Slide 15: Testbed: BW imaging, slide
4x objective
1600x1200 pixel, 1 um / pixel
RG630 filter
BW camera: all pigments – one color
Fluorescence
“White” light
Samples courtesy of Holly Bowers
160 x 160 um region
160 x 160 um region

## Slide 16: Testbed: color, net tow sample
10x objective
1600x1200 pixel, 0.4 um / pixel
Delvie 2422 filter
Color camera: ID pigment group
Fluorescence
White light
Samples courtesy of Julio Harvey
Multiple cells per slide, each in its own bubble!

## Slide 17: Comparison
Includes processing platform
Limited control of camera
Better camera control
Access to image trigger signals
Multi-camera architecture
Use of microscope objectives
Compact, low power
Need processor board
Cell phone obsolescence
Single camera?
“Cell phone level”
Entry level
High end
microscope components

## Slide 18: Next steps
Energy: sensitivity, power, exposure
Architecture
  Software: image processing
  Flow cell design
  Processing platform
Capability  requirements
  Search for middle ground
  Multidisciplinary team
Have some idea
Running out of time this year
Very important

## Slide 19: Bench top test bed
Smart phone microscope

## Slide 20: Some emerging mobile instruments
PipeCyte flow cytometer (Swalwell/UW)
  NSF funding (3 years)
Psi-Fi light-sheet imaging cytometer
  Commercial venture underway?
Mobile Imaging Flow Cytobot (Sosik/WHOI)
  Integration with Wave Glider, other mobile platforms
Wave Glider Microscope (JRF)
  MBARI/JRF collaboration project in 2016?