## Slide 1: Fish and Object Classification in Videos with Accelerated User-Guided Annotation
David Zhang, Jun Hu and Michael Piacentino
david.zhang@sri.com, jun.hu@sri.com, michael.piacentino@sri.com
March 30, 2017

## Slide 2: Agenda
Program Summary
Roadmap
Overview of Tasks
Performance Summary of Fish Detection Algorithms
Accelerated User-guided Annotations
Challenges
Future Work

## Slide 3: Project Summary
Today the job of counting fish to understand the density of fish monitored for stock assessment reasons is a very manual, time-consuming event.
Program goal is to demonstrate the capability to rapidly detect and track fish in recorded video streams. The detection and tracking process will provide an automated means of performing fish assessment by counting each fish type seen on the recorded videos.
This project will enable researchers to integrate the detection and track functionality into their own PC based video playback and analysis systems.

## Slide 4: Automated Stock Assessment
NOAA Stock Assessment Objective:
Provide automated tools to determine the quantities, size and types of different fish
Automated Stock Assessment
Approach:
Use computer vision technologies:
Fish tracking – detect presence of fish – segment each fish
Classification of the moving objects – quantities of different types of fish
Other technologies (i.e. stereo) for size estimates
Problem:
Analysis of video and still data far exceeds capabilities of human analysts
Data products not available quickly enough for use in stock assessments

## Slide 5: Roadmap
Fish
Detection
Fish Type
Detection
Accelerated
User-Guided
Annotations
Sample
videos
Sample
videos
Large quantity
of videos
Build large
Database for Classification
Sea Animal
Taxonomy
VIAME
MBARI
NOAA
FY2015
FY2016
FY2017
FY2018
VIAME
PathNet
Possible Path Future Effort
Online Stock Assessment
Web based client/server App
Online tools provide key capabilities
Detection
Tracking
Classification
Size Assessment
Regional Distribution Statistics
Optical flow
Object proposals
Deep Learning Network
Detection, Tracking, Classification
Database
Unsupervised learning
Deep Learning Network
MBARI
Others

## Slide 6: Overview of Current Tasks
Integrate classification module into the NOAA Video and Image Analytics in a Marine Environment (VIAME) program application framework.
Test classification performance using large image and annotation data sets
Enhance fish detection and classification algorithms based on results of larger data sets
Develop a semi-supervised web-based application that allow accelerated, user-guided annotations on videos.
  Provide annotating of large quantities of video streams in a short time and set up large data base for training and hierarchic classifications of sea creatures.

## Slide 7: Fish Detection and Fish Type Classification
Block diagram of object classification
Block diagram of motion segmentation

## Slide 8: Fish Detection and Fish Type Classification
# Connections
connect from input.image
to process.image
connect from process.out_image
to disp.image
# Process definition
process input
:: frame_list_input
process process
:: ProcessImage_benthosdetect
process disp
:: image_viewer
Input port
Output port
Read frame(t) from input port
Write frame(t) to output port
ROIs, types
Trained
model
# Configurations
Optical flow parameters
Object proposal parameters
ROI merge/fusion criteria
DNN inferencing parameters
Modified Non-Maximum Suppression parameters
Fish type bounding box coloring scheme
# Initialize
# Reset
# Flush
Flow
Segmentation
Object
Proposals
DNN
Inferencing
Modified
NMS
Merge Regions
of Interest
Block Diagram and Scripts to run fish classification in VIAME Framework
Matthew Dawkins, Linus Sherrill, Keith Fieldhouse, Anthony Hoogs, David Zhang, Lakshman, Prasad and Benjamin Richards, “An open-source platform for underwater image and video analytics”, WACV March, 2017.

## Slide 9: Fish Detection Review
Flow based segmentation and detection
Deep learning based
Detection

## Slide 10: Fish Type Classification Examples
Video data provided by
MBARI
Example 1
Example 2

## Slide 11: Fish Type Classification Output File
"frames": [
{
"frame_id": 0,
"frame_rois": [
{
"roi_score": 27.345077514648438,
"roi_h": 90,
"roi_x": 978,
"roi_y": 916,
"roi_label": {
"label_id": 6,
"label_name": "6: Mediaster_aequalis"
},
"roi_w": 102,
"roi_id": 0
},
{
"roi_score": 18.93919563293457,
"roi_h": 302,
"roi_x": 562,
"roi_y": 292,
………….
Output ROIed videos
and JSON file
Frame#
ROI#
Detection score#
Detection ROI#
Label #
Label string

## Slide 12
Missed:Glyptocephalus_zachirus
Merluccius_productus
Notes:
Object proposals need to be improved in handling weak features, large deformable objects.
Pulling in temporal tracking will help; above results are purely frame based.

## Slide 13: Fish Type Classification Examples
Example 1
Example 2
ROC curve

## Slide 14: Annotation Challenges
Current commercial applications do not work well for annotations of underwater video streams.
MBARI annotation scripts
Coarse annotation: observers’ records
Reviewer’s annotations
Species show-up time, time period
No ROI info, timestamp can be minutes away
Manual annotation is impossible on large video streams
Semi-supervised or user guided unsupervised annotation is possible
Blind object proposals would generate large candidates
Labeling of clusters of objects takes much less time
LabelMe
https://github.com/CSAILVision/LabelMeAnnotationTool
Javascript
Learning based
User input polygon
Frame-based
We propose:

## Slide 15: SRI Semi-supervised Annotation Method
10
20
100
……
……
0
Video Stream
database
Sample
selection
Object
proposals
Feature
generation
Blind
segmentation
Label
new set
Distance sort
user
Deep learning
training
Object
proposals
Inferencing
……
……
……
Fine-tuned
DNN model
{Object class,
Location,
Confidence
Measure}
……
time

## Slide 16: SRI Semi-supervised Annotation App Design
Blind Segment
Bundles
Easy Sorting
Hard Sorting

## Slide 17
Actinostolidae
Calliostoma_platinum
Chionoecetes_tanneri
Glyptocephalus_zachirus
Lycodes_diapterus
Mediaster_aequalis
Merluccius_productus
Porifera
Psolus_squamatus
Raja_rhina
Rathbunaster_californicus
Sebastes - 2 spp
Sebastolobus_altivelis
Strongylocentrotus_fragilis
Stylasterias_forreri
15 Fish types:
Modified Annotations from MBARI

## Slide 18
Background:
Modified Annotations from MBARI

## Slide 19: Blind Segmentations as Quick Annotations
Index | Distance | number
2 | 21.73 | 65
0 | 38.51 | 190
5 | 38.87 | 196
4 | 39.97 | 392
1 | 40.74 | 433
6 | 41.14 | 84
3 | 41.21 | 240
Sebastes_2species (149)
Sebastes - 2 spp
Precision: 100%
Recall: 65/67=97%
Blind
Segmentation
Results:
K = 7
67
82
1. User selects 1 sample: Sebastes - 2 spp
2. User then clicks “Blind Segment” and by default takes the best set
3. One iteration is sufficient

## Slide 20
Index | Distance | number
1 | 8.18 | 433
4 | 11.34 | 392
3 | 16.99 | 240
6 | 19.78 | 84
5 | 27.17 | 196
2 | 30.39 | 65
0 | 31.64 | 190
Strongylocentrotus_fragilis (83)
Strongylocentrotus_fragilis
Precision: 82/433 =18.9%
Recall: 82/83 = 98.8%
Blind
Segmentation
Results:
K = 7
1601 images
background
First iteration:
Precision: 78/81 = 96.3%
Recall: 80/81 = 98.7%
Second iteration:
Precision: 81/99 = 81.8%
Recall: 81/83 = 97.6%
Third iteration:

## Slide 21: Label New Creature Type from Blind Segmentation
Precision: 82/84 = 97.6%

## Slide 22: Challenges and Future Work
Improve object proposals
Combine temporal features with spatial features
Fast training Networks with good “memory”. It would quickly train new annotated data while not degrade its performance on the pre-trained data
Hierarchic Neural Networks that classify coarse to fine taxonomical trees: class, order, family, genius and species.
Domain Adaptation algorithms that help trained neural weights to adapt to various video noise, scene brightness and saturation, contrast change, blur and others

## Slide 23: Acknowledgement
The program was funded by NOAA Fisheries Strategic Initiative on Automated Image Analysis.
Fish data set used in the training and detection was provided by MBARI.
Thank you!