## Slide 1: Automated Stock Assessment Real-Time Image Detection and Tracking for Improved Fish Classification and Counting Year 1
Mike Piacentino
michael.piacentino@sri.com
Jan 10, 2015

## Slide 2: Agenda
Project tasks
Goals and Challenges
Overview of vision processing functions for year 1
Segmentation to enable counting and classification
Description of module interfaces
Summary of framework summaries and possible next steps

## Slide 3: Year 1 SRI Main Tasks
SRI under contract Nov 20, 2015
Main Tasks:
Package our vision based detection, segmentation and tracking algorithms as to allow them to be used by researchers to study their performance when applied to underwater fish counting scenarios.
Prior to packaging and delivery of the detection and tracking algorithms SRI will work with NOAA program team members to define the optimal application interfaces and configurations for use in the program.
Based on the interface and optimal algorithm parameters determined, SRI will modify and package the detection and track algorithms.
Test algorithm performance on existing researcher collects.
Delivery: SRI will deliver the detection and tracking module as an application module with a defined API that others can integrate into the to be defined program application framework.

## Slide 4: Automated Stock Assessment
End Goal:
Determine the quantities, size and types of different fish automatically
Approach:
Year 1:
Moving object tracking – detect presence of fish
Segment fish from background through enhancement, stereo, flow, etc…
Stereo for size measurements
Year 2:
Classification of the moving objects – quantities of different types of fish
Incorporate semi-automated learning
Automated Stock Assessment

## Slide 5: Challenging conditions
Cameras drop by a boat and are floating at a fixed location to do fish distribution survey.
Moving cameras are dragged along gas pipelines looking at fish populations.
Automated Stock Assessment

## Slide 6: Automated Stock Assessment
Automated Stock Assessment
Proposed Algorithms:
Fish Detection
Fish Numbering
Fish Classification
Background modeling
+Optical flow*
Automated
segmentation
Tracking/numbering
Objectiveness
Fish / no-fish
training
Tracking/numbering
Fish / no-fish
classification
Fish type
training
Objectiveness
Fish type
classification
Numbering/Fish_type
* Yellow boxes indicate the work we have done in year 1 so far.
Stereo added for moving cameras

## Slide 7: Automated Stock Assessment
Approach Year 1:
Integrate front end enhancement processing to maximize fish detection in water.
Integrate background modeling and optical flow to automate fish segmentation.
Use stereo disparity and color information and optical flow to automate fish segmentation in the moving cameras.
Analyze false positives and false negatives from the conventional image processing methods.
Provide module that does segmentation and initial fish counting.
Measure performance comparing to human detection.

## Slide 8: Fish Segmentation – Background Modeling
Background Modeling in Motion Tracker
Single modal Gaussian Mixture Model for background extraction.
Fish Detection
Original videos
Average background
on 1000 images

## Slide 9: Fish Segmentation – Fish Mask Creation
Background Modeling in Motion Tracker
Single modal Gaussian Mixture Model for background extraction.
Fish Detection
Original videos
Masks generated from the
background modeling

## Slide 10: Pre-processing Enhancement
Underwater videos suffer from poor visibility due to absorption and scattering effects.
In common sea water, fish 10 meters away are almost indistinguishable due to faded contrast and colors.
Luminance-only videos are taken in the sea water for higher sensitivity and utilizing near IR signals for further depth.
The contrast between fish and water is often low.
Input
image
Dehaze
If color
Global
enhancement
Local
enhancement
Pre-process Enhancement

## Slide 11: Fish Segmentation – Enhanced imagery, improved masks
Background Modeling in Motion Tracker
Single modal Gaussian Mixture Model for background extraction.
Contrast enhanced source images for BG Modeling
Fish Detection
Enhanced videos
Masks generated from the
background modeling

## Slide 12: Fish Segmentation – Graph Based Approach
Fish Detection
Video segment from the original source
Video segment from the enhanced source
video_segment algorithm by GeorgiaTech
M. Grundmann et al.,
Efficient Hierarchical Graph Based Video Segmentation,
CVPR 2010
Method being tried as a means to further improve segmentation. Initial results show need for some optimization for it to help.

## Slide 13: Fish Segmentation – Improvement with Flow
Motion Flow for fish segmentation (after CN and BM)
Fish Detection
Flow vector map
Flow orientation color map
Segmentation result

## Slide 14: Fish Segmentation – Improvement with Flow
Motion Flow for fish segmentation (after CN and BM)
Fish Detection
Flow vector map
Flow orientation color map
Segmentation result

## Slide 15: Fish Segmentation – Stereo
Stereo for improved segmentation and size determination
Fish Detection
Segmentation performance improvement
- Need to understand better the calibration parameters for each of the datasets with stereo data.

## Slide 16: Function Diagram for Automated Detection and Tracks
Background modeling, segmentation and flow block diagrams
Input
image
Dehaze
If color
Global
enhancement
Local
enhancement
Pre-process Enhancement
Image
input
Preprocess
enhancement
Background
statistics
Optical flow
computation
Foreground
subtraction
Mag-Orient
binning
Thresholding
and grouping
Regions
and indices
Tracking
Automated Detection and Tracks

## Slide 17: Function Diagram for Automated Detection and Tracks
Video streams
(color, mono, stereo, etc)
Configuration (System information)
Pre-process
enhancement
Detection &
tracks
Timestamps
Timestamp
Frame#
# of fishes
ROI of fish
Enhanced images
Background images
GUI controls
Color/gray, stereo/mono videos are configured by the external configuration input.
Pre-process enhancement and detection tracks are independent functions. Their connections are configured by the external configuration input.
GUI controls are per function-block. They are loaded up by the external configuration input.
Output is configured by the external configuration input.

## Slide 18: Features of Detection and Tracks Algorithm
Pros
Our implementation approach is based on the background modeling when camera is still or moves slowly. Fish segmentation combines the background model and cues from the optical flow vectors.
In the moving scenario, stereo cameras are preferred to generate depth. Fish segmentation combines the depth and the motion cue.
Flow and other methods can be used to further improve segmentation
From the stereo camera, size of the fish can be more easily measured.
Cons
Configurations for detection and tracks likely change from one condition to the other.
False positives and false negatives can be high.
Not accurate when fishes overlap.

## Slide 19: Conclusion and Future Work
Algorithm framework and algorithm development
  We have reviewed initial object segmentations based on background modeling and optical flows.
  We also discussed the potential improvement using deep learning.
Challenges will need attention
  Background, Camouflage, Silt in water, Occlusions, Stationary fish
Next Steps moving forward
  Process a larger set of captured datasets
  Need to finalize stereo alignment parameters
  Improve robustness of algorithms with above challenges
  Improve object segmentations in both single and stereo cameras
  Speed up fish/no-fish training by using object ROIs
  Develop more efficient and robust object detection and tracking
  Extend counting and classification framework - Train Convolutional Neural Networks (CNN) with fish type classification features

## Slide 20: Summary of Framework Calls

## Slide 21: Framework Summary - 1
Video and metadata formats:
While there are many types of formats used, we should consider the idea of standardizing on a few types. Also, for metadata it may be beneficial to setup a format that is more uniform even if all the data is not collected.
Support both video and still image processing and each has different associated processing and analytics.
With respect to metadata we need to understand better from the users what other metadata we want to capture and from the developers what other metadata could help/enhance the analytics performance.
Real-time vs batch
Most folks use batch processing today and processing times take 2X-16X the record times. Since often a person is in the loop on processing and annotations shortening the processing times could greatly reduce the cost of processing data.
Common Framework versus Previous
It was recognized that some folks have put a good deal of efforts into their current frameworks but longer term it will benefit not only to these users but all users to move to a common framework. In a shared common framework it is much easier to extend and share capabilities to ensure all users advance their capabilities. It will be important that a new framework approach also has support and user training capabilities.

## Slide 22: Framework Summary - 2
Development languages and Operating Systems
It was mostly agreed upon that we would not restrict programming languages for developers but we want to define some form of common module interface to allow for easy and reliable interfacing between modules in the framework.
Additionally it was acknowledged that yes Linux may be more secure over Windows there was not direct push to go to either of the two.
WEB-based vs. Custom GUI framework
Going with a WEB-based solution allows us to worry less about the OS.
Even though a few folks have concerns about the security of a WEB-based framework there may be more advantages and we should consult with IT folks to understand the tradeoffs.
A web-based solution allows for easier rollouts, updates and support.
A WEB-based solution provides easy remote access and avoids the issues of installing new SW on systems with permission issues introduced by individual IT groups.
Noted that scalability and flexibility are still key requirements of a WEB-based solution.
A WEB-based solution would likely better support a spiral rollout schedule and faster time to the users hands.

## Slide 23: Framework Summary - 3
Overviews of current capture tools
It was discussed that to aid the developers it would be beneficial for the developers to understand the tools and their configuration/parameters for both capture and annotation. Ben suggested organizing short WEB-X meetings.
Overall main goals of tools
There were numerous suggestions on capabilities and things the tools could enable for users but direction from the meeting is to focus on these key goals.
  Abundance/numbers of items being counted
  Size of items being measured
  Sorting the items into classes
  A long term goal of determining the specifies
Work Flow Diagram
It was agreed upon that it is important to develop a system workflow diagram. This diagram should illustrate the full flow from capture through results and show the steps and interfaces between each of the system flow stages (e.g. detection, classification, annotation, etc.). It was not determined who would help contribute to this diagram as of yet.

## Slide 24: Framework Possible Paths Forward
Two framework candidates that may require less upfront work
  HT-CONDOR
    CONDOR is an open Fluid Development environment
    Is a knowledge based tools for consistency
    Used mainly for underwater analysis
    Have supporting annotation tools (VARS – sits on database of videos and stills)
    High level modules connection
    VARS sits on databases of video and stills
  KWIVER
    Uses some OpenCV functions but not built on OpenCV
    Provides a full video pipeline tool capability
    Not yet tailored for underwater video analysis
    Mix of MATLAB, Python, C++, JAVA; Currently just supports ffmpeg
    Can support real-time down the road
    Still a work in progress
Others tools exist (e.g. DARPA VMR, ITK, etc…)

## Slide 25: Possible Open Source Framework to Leverage – 1 - MBARI toolset
MBARI has developed a framework for underwater image/video analysis, based on HT-CONDOR (http://research.cs.wisc.edu/htcondor/) open source workload management system. MBARI integrated analytic modules to do preprocessing, event detection (C++), database interaction (XML), classification (matlab), results editor and visualizer, and so forth, with workflows distributed over a compute cluster, HaaS, or VM cloud.
Expert at MBARI on this technology is
Contact: Danelle Cline (dcline@mbari.org);
Our work is offered here: https://code.google.com/p/avedac/ and
described here: http://prezi.com/ho8wgz76l50l/avedac/ and
here: http://www.mbari.org/aved/

## Slide 26: Possible Open Source Framework to Leverage – 1 - MBARI toolset
The MBARI framework includes the open-source Video Annotation and Reference System (VARS), a software interface and database system that provides tools for describing, cataloging, retrieving, and viewing the visual, descriptive, and quantitative data associated with video archives. Information about VARS is available at:
http://www.mbari.org/vars/
http://www.mbari.org/twenty/VARS.htm
http://vars.sourceforge.net/
Contact: Brian Schlining (brian@mbari.org)

## Slide 27: Possible Open Source Framework to Leverage – 2 - KWIVER
The Kitware Image and Video Exploitation and Retrieval (KWIVER) toolkit is a collection of software tools designed to tackle challenging image and video analysis problems and other related challenges. Recently started by Kitware’s Computer Vision and Scientific Visualization teams, KWIVER is an ongoing effort to transition technology developed over multiple years to the open source domain to further research, collaboration, and product development.
Contact: Anthony Hoogs (anthony.hoogs@kitware.com);
Existing KWIVER Open Source Repositories
Existing KWIVER Government Open Source Repositories (on Forge.mil)
Existing Data Sets
Planned Public Open Source Repositories & Data Sets

## Slide 28: Possible Open Source Framework to Leverage – 2 - KWIVER

## Slide 29: Possible Open Source Framework to Leverage – 2 - KWIVER

## Slide 30: Automated Stock Assessment Real-Time Image Detection and Tracking for Improved Fish Classification and Counting Year 2
Mike Piacentino
michael.piacentino@sri.com
Jan 11, 2015

## Slide 31: Year 2 Project Proposal - 2015
SRI International proposes to extend our capabilities of fish detection, tracking and classification to further enhance robustness of detection performance through addition of deep learning algorithms.
The inclusion of the deep learning algorithms will enable operation in widely varying environments, platforms, sensors (stereo and mono) and lighting conditions.
Leveraging the image processing framework the NOAA team is developing in year 1, SRI shall provide additional capabilities available for integration into this common framework.
We shall incorporate automated classification methods to allow for counting the detected fish species. Robust counting will be enabled through deep learning and classification approaches such as Convolutional Neural Networks (CNN). The deep learning algorithms will support learning from existing ImageNet pre-trained data as well as other learning datasets. In year 2 SRI shall deliver quarterly software capability enhancements to the existing year 1 framework allowing for iterative feedback, testing and requests from researchers over the year.

## Slide 32: Year 1: Function Diagram for Automated Detection and Tracks
Background modeling, segmentation and flow block diagrams
Image
input
Preprocess
enhancement
Background
statistics
Optical flow
computation
Foreground
subtraction
Mag-Orient
binning
Thresholding
and grouping
Regions
and indices
Tracking
Automated Detection and Tracks
Feed Year 2 Deep Learning

## Slide 33: Deep Learning to Support Limitations in Segmentation
Detection limitations
The detection algorithms using background modeling and optical flows can have limitations. For example:
The fish segments are error prone.
False positive due to background noise and environmental light change.
True negative with lack of contrast in segmentation.
Difficult detecting stationary fish.
Improvements of fish detection by using Deep Learning
Deep learning approach relaxes the stringent requirement in fish detection. Fractional segments are well accepted as the input image regions in fish classifications since the result would automatically exclude the false regions.
Much reduced false positives and true negatives from the deep learning network outputs.
Easy integration into the defined framework since the training and classification modules are independent, and are portable and well interfaced.

## Slide 34: Visual Media Reasoning (VMR)

## Slide 35: Visual Media Exploration and Search Index-Tag-Find

## Slide 36: Visual Media Exploration and Search Use Case – Ease exploration of large quantities of image/video data
Millions of images and videos
Cell-phones, Social media
Surveillance cameras
Data Collection
Probe-free clusters of similar images

## Slide 37: Exploring visual data - Clustering

## Slide 38
Probe
Retrieved
Results
Sample Results: Symbol/Logo Retrieval

## Slide 39: Leveraging VMR for NOAA Needs
VMR developed many different reasoning, learning and classification algorithm solutions
One such algorithm we very recently tested on fish is CNN (Convolutional Neural Networks)
Many more features of VMR can be pulled in to NOAA (e.g. clustering) to really help the researchers

## Slide 40: Proposed Improvement of Features of Detection and Tracks Algorithm by using Deep Learning
Sample
Video streams
(color, mono, stereo, etc)
Configuration
Pre-process
enhancement
Detection &
tracks
Timestamps
GUI controls
Semi-automate
Training
Video streams
(color, mono, stereo, etc)
Configuration
Pre-process
enhancement
Detection &
tracks
Timestamps
GUI controls
Classification
Timestamp
Frame#
ROI of fish
Fish Types
# of fish
Manual
annotation
of fish type
Trained
CNN
coefficients

## Slide 41: Proposed Improvement of Features of Detection and Tracks Algorithm by using Deep Learning (CNN as an initial test)
In training, each fish region is segmented based on the foreground mask and optic flow vectors. Overlapped fish regions are excluded by the motion vector dominance.
In training, the training criteria can be fish/no-fish. Then the trained coefficients would make the CNN output a fish/no-fish binary value.
In classification, the proposed fish regions are flexible and don't not to be perfect. The CNN would generate weights of each trained classes. The output would not only tell if the object is a fish, but also tell the type of fish.

## Slide 42: Fish type detection– First=> Training by CNN
Training part of the network that adds classifications to types of fish. The new category would detect what type of fish.
Use Image processing to detect well-defined ROIs of fishes from each frame. Minimize the manual selection of regions of fish. Avoid fish overlap. Manual annotations of the type of fish per ROI.
Feed in fish and non-fish ROIs to CNN. CNN back propagations will train the coefficients in the network based on the fish/non-fish ground truth.
Sample
Video streams
(color, mono, stereo, etc)
Configuration
Pre-process
enhancement
Detection &
tracks
Timestamps
GUI controls
CNN
Semi-automate
Training
Manual
annotation
of fish type
Trained
CNN
coefficients
Fish
ROIs

## Slide 43: Fish type detection – Second => Classification by CNN
Video streams
(color, mono,
stereo, etc)
Configuration
Pre-process
enhancement
Detection &
tracks
Timestamps
GUI controls
CNN Fish type
Classification
Timestamp
Frame#
ROI of fish
# of fish
per type
Objectiveness
Feed in single image or video stream. Detection, tracking and segmentation generates region of interest of possible candidates.
Objective proposals can be relaxed by combining multiple segments.
Fish type classification provides scores of each detection on ROI.

## Slide 44: Fish Classification
Fish Detection using Convolutional Neural Network
Fish Detection
Convolutional Neural Network
Fish/ Not Fish
Convolutional Neural Network (CNN): Alexnet trained on Imagenet with 1.2 million images and 1000 classes
Fish/ Not Fish: If any of the top 5 predicted classes from CNN contain a fish class, we classify that bounding as a fish
Feed in ROI for fish classification
Fish
Non-fish

## Slide 45: Deep Learning using Convolutional Neural Network(CNN)
CNN is a feed-forward multi-layer artificial neural network where the individual neurons are tiled in such a way that they respond to overlapping regions in the visual field.
Deep network (7 layers)
Trained with stochastic gradient descent on two NVIDIA GPUs for about a week
650,000 neurons
60,000,000 parameters
630,000,000 connections
Final feature layer: 4096-dimensional
CNN results on ImageNet (automatic recognition of 1000 categories of objects in images)

## Slide 46: Fish Classification using pre-trained data from ImageNet
n01491361 tiger shark, Galeocerdo cuvieri
n02514041 barracouta, snoek
n01484850 great white shark, white shark, man-eater, man-eating shark, Carcharodon carcharias
n02074367 dugong, Dugong dugon
n01496331 electric ray, crampfish, numbfish, torpedo
n01491361 tiger shark, Galeocerdo cuvieri
n01873310 platypus, duckbill, duckbilled platypus, duck-billed platypus, Ornithorhynchus anatinus
n01496331 electric ray, crampfish, numbfish, torpedo
n01484850 great white shark, white shark, man-eater, man-eating shark, Carcharodon carcharias
n01494475 hammerhead, hammerhead shark
n04152593 screen, CRT screen
n01930112 nematode, nematode worm, roundworm
n09472597 volcano
n02066245 grey whale, gray whale, devilfish, Eschrichtius gibbosus, Eschrichtius robustus
n03782006 monitor
n01930112 nematode, nematode worm, roundworm
n04266014 space shuttle
n04152593 screen, CRT screen
n04592741 wing
n03291819 envelope
n04270147 spatula
n04067472 reel
n03041632 cleaver, meat cleaver, chopper
n03961711 plate rack
n04286575 spotlight, spot
n01955084 chiton, coat-of-mail shell, sea cradle, polyplacophore
n01990800 isopod
n02093859 Kerry blue terrier
n02093647 Bedlington terrier
n03207743 dishrag, dishcloth
Fish, true positive
Fish, true positive
Fish, true positive
Fish,
False negative
Non-fish, true negative
Non-fish, true negative

## Slide 47: Fish Classification using pre-trained data from ImageNet
Fish Detection
Out of total 53 images (fish and non-fish):
True Positives: 39 (fish identified as fish)
False Positives: 4 (fish not identified as fish)
False Negatives: 9 (non-fish identified as fish)
True Negative: 1 (non-fish identified as non-fish)
Overall Accuracy: 75.47%
Result summary from previous slide on pre-cropped fish images along with non-fish images
Used a generic training set no tuning of CNN network for fish

## Slide 48: Proposal Goals
Objective proposal
Refine fish segmentation algorithms for both single and stereo cameras.
CNN fish detection using CNN
Use CNN Caffe on GPU to train generic fish category
Use CNN Caffe to classify fish in real-time videos
Analyze success/error rate
CNN fish type detection using CNN
Use CNN Caffe on GPU to train fish type category – need help on annotation
Use CNN Caffe to classify fish types in real-time videos
Analyze success/error rate
Framework
Adapt modularity to proposed framework
Goal:
Improved fish detection accuracy and obtain finer classifications
Implement interface to adapt to the proposed framework

## Slide 49: Backup

## Slide 50: SVR Image/Video Explore and Search System Configurations
Configuration | Features
Enterprise For large-scale cluster/cloud architecture | Web-services based API Asynchronous communications between servers and multiple workers Handles datasets of several million images/videos Indexing time for several million images/videos: 10-12 hours Near real-time search (5 seconds to a few minutes – after indexing) Near real-time probe-free clustering (after indexing) Multiple simultaneous users
Desktop For a small cluster/cloud architecture | Web-services based API Asynchronous communications between 1 server and 3+ workers Handles > 1M+ image/video datasets Indexing time: 100K images/videos = ~6 hours; 1M = ~10-12 hours Near real-time search (10 seconds to several minutes) Near real-time probe-free clustering 2 – 3 simultaneous users
Field For a portable single laptop system | Web-services based API Can handle datasets of up to 1M images/videos; typical = 1K – 100K Indexing time for 1K images: ~30 minutes Near real-time search (minutes – after indexing) Near real-time probe-free clustering (after indexing) 1 user Low memory footprint
50