## Slide 1: 6000m Spherical Ti Pressure Vessel Design Review
Gene Massion
March 2011

## Slide 2: Requirements & Goals
Increase safe working depth to 6000 meters
Same ID = 8.0”
  Approximately same interior volume
  Weight/displacement ration < 1.0
    Current design W/d = 0.95, Glass sphere = 0.41
8 minM connectors + 10 minK
1 ODI connector w/reduced number of minK/M
1 SAE #4 port
Some kind of mounting “tabs”
Minimize number of fastener (goal)
Standard stretch on O-rings (goal)
Reduce 1) machining, 2) casting, 3) pattern costs (goal)

## Slide 3: Existing Design

## Slide 4: Initial Design Iterations
One piece connectors at “top”
Two piece connector hat at “top”

## Slide 5: Preferred design
Displacement = 97.3 lbf
Weight/Displ. = 0.93
Wet Weight = -6.34 lbf

## Slide 6: Pros and Cons

## Slide 7: Structural Analysis Roark vs FEA
Note: No significant change in values at finer FEA meshes

## Slide 8: FEA (symmetry at bolt circle)

## Slide 9: FEA (bolted)

## Slide 10: Distortion at O-ring

## Slide 11: Buckling
1 < BLF
Buckling not predicted. The applied loads are less than the estimated critical loads. Buckling is not expected.

## Slide 12: Roark Buckling Calculation

## Slide 13: To Do List
Pick a preferred design
Optimize W/D ratio and weight in water
Fix local high stress areas
Make sure connector bores don’t distort unacceptably for proper sealing
Re-do FEA with outer O-ring failure
Equalize bearing pressure at dual O-ring grooves
Work with Oremet Wah-Chang (and Jon) to optimize manufacturability
Generate drawings
Buy 1, 10, 100(?)
Pressure test