## Slide 1: One-Stop Shopping & Upper Water Column Data Visualization
Mike McCann
CANON Planning meeting
18 February 2010

## Slide 2: CF* Point Observation Data
Point observation A data measurement at a specific time and location. Each kind of measured data is placed in a data variable. The time and location values are placed into coordinate variables and auxiliary coordinate variables.
* Climate Forecast conventions (for data in NetCDF files)

## Slide 3: CF Point Observation Data
Point feature types (Common Data Model) Reflect the connectedness of common observational datasets in the earth sciences
  Point bucket measurement
  StationTimeSeries Meteorlogical sensors on a mooring
  Trajectory AUV, drifter
  Profile Shipboard CTD casts, Niskin bottle data
  StationProfile Mooring microcat string, ADCP
  Section collection of profiles along a trajectory, processed AUV data

## Slide 4: OPeNDAP* Data Structures
Grid
  Examples: Mooring data (gridded in time and depth), Model output (gridded on x,y,z,t axes)
  Looks a lot like CF-NetCDF
  DDS for Mooring CTD String TEMP variable (stationProfile CDM type):
  Grid {
  ARRAY:
  Float32 TEMP[TIME = 2523][DEPTH = 11][LATITUDE = 1][LONGITUDE = 1];
  MAPS:
  Float64 TIME[TIME = 2523];
  Float64 DEPTH[DEPTH = 11];
  Float64 LATITUDE[LATITUDE = 1];
  Float64 LONGITUDE[LONGITUDE = 1];
  } TEMP;
* Open-source Project for a Network Data Access Protocol (a way to efficeintly serve NetCDF and other data over the web)

## Slide 5: OPeNDAP Data Structures (cont.)
Sequence (example: DRDS for BOG’s BTCD table)
Dataset {
Sequence {
Int32 CTD_BOTTLE_ID;
String CRUISE;
Int32 EXPD;
Int32 SEQ;
Int32 DEPTH;
Int32 BOTTLE;
String PROJECT;
String CTRB_ID;
String PLATFORM;
...
Float64 pot_tmp;
Float64 OxyT;
Float64 OxyC;
Float64 TransV;
Float64 TransBeam;
Float64 POT_TMP2;
Float64 OxyV;
Float64 ISUS_NO3;
} BCTD;
} test;

## Slide 6: OPeNDAP Data Structures (cont.)
Sequence & Structure together (example: dapper)
Dataset {
Sequence {
Float32 LATITUDE;
Float64 JULD;
Float32 LONGITUDE;
Int32 _id;
Sequence {
Float32 TEMP_DOXY_ADJUSTED;
Float32 CNDC_ADJUSTED_ERROR;
...
Float32 BPHASE_DOXY;
Float32 PRES_DOXY_ADJUSTED_QC;
} profile;
Structure {
String PLATFORM_NUMBER;
String PROJECT_NAME;
String PI_NAME;
...
} attributes;
Structure {
Structure {
Float32 valid_range[2];
} PRES;
} variable_attributes;
} location;
Structure {
Float32 lon_range[2];
Float32 lat_range[2];
Float32 depth_range[2];
Float64 time_range[2];
} constrained_ranges;
} argo_all;

## Slide 7: Data System Architecture
AUVCTD
ROVCTD
Interoperation
BOG
OASIS
SIAM
QC
SSDS
NetCDF
File Format
CF-1.1
Meta Mgmt
Telemetry
Conventions
Access
OceanSITES
OPeNDAP
THREDDS/OPeNDAP
3rd party
MOQuA
LAS
Access Tools
Presentation
Custom
Work proposed for 2010
RDBMS/SQL
Mooring
Data Processing

## Slide 8: Data System Architecture
AUVCTD
ROVCTD
Interoperation
BOG
OASIS
SIAM
QC
SSDS
NetCDF
File Format
CF-1.1
Meta Mgmt
Telemetry
Conventions
Access
OceanSITES
OPeNDAP
THREDDS/OPeNDAP
3rd party
MOQuA
LAS
Access Tools
Presentation
Custom
Work proposed for 2010
RDBMS/SQL
Mooring
Data Processing
Station & StationProfile
Profile
Trajectory
Common Data Model scientific data type

## Slide 9: OPeNDAP Conundrum
Client tools
  Plenty of good tools for working with Grid data structures, mainly because it looks a lot like NetCDF and those tools have been around a while.
  Tools for effectively dealing with Sequence/Structure are now becoming available, e.g. pydap, dapper/dchart, …

## Slide 10: Where does RDBMS/SQL fit?
Powerful geospatial enhanced database systems now exist, e.g. PostgreSQL, MS SQL Server 2008, MySQL, etc.
Web servers: mapserver, geoserver, etc.
Google Earth can be used to display disparate data from databases
Development environments:
  In the beginning we had Sybase’s Data Work Bench, now we have Enterprise Manager, or SQL “wizards” built into desktop products like ESRI ArcGIS
  They are “Software Engineer” level tools

## Slide 11: Where does RDBMS/SQL fit? (cont.)
Development environments (cont.)
  Would like to have a “Matlab-like” environment for working with RDBMS/SQL data
Benefits
  More complex data structures than can be served via OPeNDAP
  Query on data values and spatial parameters
  Can index any column providing high-performance search
  Provide foundation for spatial analysis (with geospatial extensions)

## Slide 12: Upper Water Column Data Visualization project
Follow-on to 2009 One-Stop Shopping project
Continue to work on developing infrastructure for providing uniform access to RDBMS/SQL and OPeNDAP Data
Build a geospatial-enabled database for MBARI Upper Water Column Data
Develop example query tools that deliver products through Google Earth

## Slide 13: Conceptual Data Flow Diagram

## Slide 14: Conceptual Data Flow Diagram
Scope of Upper Water Column Data Visualization project work in 2010